## Slide 1: Bomberman
Fredrik Ahlberg – ael09fah@student.lu.se
Magnus Hultin – ael08mhu@student.lu.se
Adam Johansson – rys08ajo@student.lu.se

## Slide 2: Concept

## Slide 3: Proposed design

## Slide 4: Actual Design

## Slide 5: GPU

## Slide 6: GPU
Up to 64 16x16px sprite bitmaps
Up to 64 16x16px tile bitmaps
Up to 64 palettes, each containing 16 color combinations
Tilemap is 16x14 tiles, supports scrolling
Sprites and tiles may be flipped
Up to 512 sprites on screen at any time

## Slide 7: Gamepad I/F
Real Nintendo 8-bit gamepads
Shift registers in gamepads are polled by hardware and is put into regs.

## Slide 8: Sound generator
Takes 8-bit PCM data values (raw audio)
2048 sample ring-buffer
39,1 KHz sample-rate
PWM signal generated @ 391 KHz
Sound data stored in SPI flash
Music and sound effects are mixed in software

## Slide 9: Memory Allocation
GPU - 13 BRAMs
MicroBlaze - 16 BRAMs, 32KB
Sound buffer - 1 BRAMs
SPI flash – 9 MB used for music, sound effects, graphics

## Slide 10: Software
Game logic is updated during Vblank interrupts @ 60Hz (~1.5 ms window)
Music is mixed and buffered inbetween interrupts
Pseudo-random generator is seeded by gamepad input timing
Total RAM-usage: 27 KB

## Slide 11: Emulator and Editor
Bitmaps and palettes were generated by us using a custom tool
Emulator was created to test and develop software in parallell with hardware

## Slide 12: Conclusion
Fun and rewarding project!
Hard to debug software running on FPGA
Only one computer can use chipscope!?
Challenge to parallellize workload, but…
Used 2 development boards
Used Git for version control
Emulator for software testing

## Slide 13: Questions?