## Slide 1: Shadows and Reflections in Real Time
Tomas Akenine-Möller
Department of Computer Engineering
Chalmers University of Technology
Slides co-developed with Eric Haines

## Slide 2: Why shadows?
More realism and atmosphere
Image courtesy of BioWare
Neverwinter Nights

## Slide 3: Another example
Blade of Darkness
Image courtesy of Codemasters & Rebel Act

## Slide 4: Why shadows?
More clues about spatial relationships
Orientation & gameplay

## Slide 5
Receiver
Definitions
Light sources
Shadow creators and receivers
Light source
Creator
Creator and
receiver

## Slide 6
Definitions
Light source types
point source
umbra
area source
umbra
penumbra

## Slide 7
Example: hard vs soft shadows

## Slide 8
Ways of thinking about shadows
As separate objects (like Peter Pan's shadow)
As volumes of space that are dark
As places not seen from a light source looking at the scene
Note that we already "have shadows" for objects facing away from light

## Slide 9: Store precomputed shadows in textures
Images courtesy of Kasper Høy Nielsen.

## Slide 10: Two major algorithms that can render shadows onto arbitrary geometry
Shadow mapping and shadow volumes
  Focus on shadow volumes, because currently most popular, and works on most hardware
Works in real time…
Shadow mapping is used in Pixar’s rendering software
Render from light’s view (white is far and black is near)

## Slide 11
Using the Shadow Map
When scene is viewed, check viewed location in light's shadow buffer
  If point's depth is (epsilon) greater than shadow depth, object is in shadow.
shadow
depth map
For each pixel, compare
distance to light with
the depth stored in
the shadow map

## Slide 12
The Result

## Slide 13: Shadow volumes Most popular method for real time
Shadow volume concept
Create volumes of space in shadow from each polygon in light.
Each triangle creates 3 projecting quads

## Slide 14
Using the Volume
To test a point, count the number of polygons between it and the eye.
If we look through more frontfacing than backfacing polygons, then in shadow.
frontfacing
backfacing

## Slide 15: Shadow volume algorithm uses stencil buffer
Stencil what?
Is just another buffer (often 8 bits per pixel)
When rendering to it, we can add, subtract, etc
Then, the resulting image can be used to mask off subsequent rendering
Stencil
Buffer
Mask
result
Rendered
image

## Slide 16
How to implement shadow volumes with stencil buffer
A four pass process [Heidmann91]:
  1st Pass: render the scene with just ambient lighting.
  Turn off updating Z-buffer and writing to color buffer (i.e. Z-compare, draw to stencil only).
  2nd pass: render front facing shadow volume polygons to stencil buffer, incrementing count.
  3rd pass: render backfacing shadow volume polygons to stencil, decrementing.
  4th pass: render diffuse and specular where stencil buffer is 0.

## Slide 17
Shadow Volume Example
Image courtesy of NVIDIA Inc.

## Slide 18
Merging Volumes
Edge shared by two polygons facing the light creates front and backfacing quad.
This interior edge makes
two quads, which cancel out

## Slide 19
Silhouette Edges
From the light’s view, caster interior edges do not contribute to the shadow volume.
Finding the silhouette edge gets rid of many useless shadow volume polygons.

## Slide 20: Planar reflections
We’ve already done reflections in curved surfaces with environment mapping
Does not work for planar surfaces
Planar reflections are important, because they too give clues about spatial relationships and increases realism
Based on law of reflection:
  Incoming angle is equal to outgoing angle

## Slide 21: Planar reflections
Assume plane is z=0
Then apply glScalef(1,1,-1);
Effect:
z

## Slide 22: Planar reflections
Backfacing becomes front facing!
Lights should be reflected as well
Need to clip (using stencil buffer)
See example on clipping:

## Slide 23: Planar reflections
How should you render?
1) the ground plan polygon into the stencil buffer
2) the scaled (1,1,-1) model, but mask with stencil buffer
3) the ground plane (semi-transparent)
4) the unscaled model

## Slide 24: Final slide Another example
Image courtesy of Kasper Hoey Nielsen
Instead of the scale-trick, you can reflect the camera position and direction in the plane
Then render reflection image from there

## Slide 25: If we got time
Stencil shadow demo