## Slide 1: Graphics Hardware
Tomas Akenine-Möller
Department of Computer Engineering
Chalmers University of Technology

## Slide 2: Graphics hardware – why?
About 100x faster!
Another reason: about 100x faster!
Simple to pipeline and parallelize
There is currently only hardware for triangle rasterization with texturing (e.g., OpenGL acceleration)
Ray tracing: there are research architetures, and one commercial product
  More to come!

## Slide 3: Today’s topics
The basics of ”perspective correct texturing”
Background on graphics hardware
The architecture of the XBOX
The architecture of the KYRO
There is very little documentation on graphics architectures…

## Slide 4: Perspective-correct texturing
How is texture coordinates interpolated over a triangle?
Linearly?
Linear interpolation
Perspective-correct interpolation
Perspective-correct interpolation gives foreshortening effect!
Hardware does this for you, but you need to understand this anyway!

## Slide 5: Recall the following, and then we change notation a bit
Before projection, v, and after p (p=Mv)
After projection pw is not 1!
Homogenization: (px /pw , py /pw , pz /pw , 1)
Rewrite and change notation to:
  w=pw
  And instead use: (pxw , py w , pz w , w)
  After homogenization: (px , py, pz, 1)
Also, remember that visible points, (px , py, pz, 1), are inside a unit-cube:
  (-1,-1,-1)  (1,1,1)

## Slide 6: Texture coordinate interpolation
Linear interpolation does not work
Rational linear interpolation does:
  u(x)=(ax+b) / (cx+d)
  a,b,c,d are computed from triangle’s vertices (x,y,z,w,u,v)
Not really efficient
Smarter:
  Compute (u/w,v/w,1/w) per vertex
  These quantities can be linearly interpolated!
  Then at each pixel, compute 1/(1/w)=w
  And obtain: (w*u/w,w*v/w)=(u,v)
  The (u,v) are perspectively-correct interpolated
Need to interpolate shading this way too
  Though, not as annoying as textures
Since linear interpolation now is OK, compute, e.g., (u/w)/x, and use this to update u/w when stepping in the x-direction (similarly for other parameters)

## Slide 7: Background: Graphics hardware architectures
Evolution of graphics hardware has started from the end of the pipeline
  Rasterizer was put into hardware first (most performance to gain from this)
  Then the geometry stage
  Application will not be put into hardware!
Two major ways of getting better performance:
  Pipelining
  Parallellization
  Combinations of these are often used

## Slide 8: Briefly about pipelining
In GeForce3: 600-800 pipeline stages!
  57 million transistors
  Pentium IV: 20 stages, 42 million transistors
Newer cards:
  Radeon 9700: 110M transistors
  GeForce FX 5800: 125 M transistors, 500 MHz
Ideally: n stages  n times throughput
  But latency increases!
  However, not a problem here
    Chip runs at about 200 MHz (5ns per clock)
    5ns*700=3.5 s
    We got about 20 ms per frame (50 frames per second)
Graphics hardware is simpler to pipeline because:
  Pixels are (most often) independent of each other
  Few branches and much fixed functionality
  Don’t need high clock freq: bandwidth to memory is bottleneck
    This is changing with increased programmability
  Simpler to predict memory access pattern (do prefecthing!)

## Slide 9: Parallellism
”Simple” idea: compute n results in parallel, then combine results
GeForce FX 5800: 8 pixels/clock, 16 textures/clock
  With a pipeline of several 100 stages, there are many pixels being processed simultaneously
Not always simple!
  Try to parallelize a sorting algorithm…
  But pixels are independent of each other, so simpler for graphics hardware
Can parallellize both geometry and rasterizer:

## Slide 10: Taxanomy of hardware
Need to sort from model space to screen space
Gives four major architectures:
  Sort-first
  Sort-middle
  Sort-Last Fragment
  Sort-Last Image
Will describe these briefly, and then focus on sort-middle and sort-last fragment (used in commercial hardware)

## Slide 11: Sort-First
Sorts primitives before geometry stage
  Screen in divided into large regions
  A separate pipeline is responsible for each region (or many)
G is geometry, FG & FM is part of rasterizer
  A fragment is all the generated information for a pixel on a triangle
  FG is Fragment Generation (finds which pixels are inside triangle)
  FM is Fragment Merge (merges the created fragments with various buffers (Z, color))
Not explored much at all

## Slide 12: Sort-Middle
Sorts betwen G and R
Pretty natural, since after G, we know the screen-space positions of the triangles
Most hardware uses this!
  Examples include InfiniteReality (from SGI) and the KYRO architecture (from Imagination)
Spread work arbitrarily among G’s
Then depending on screen-space position, sort to different R’s
  Screen can be split into ”tiles”. For example:
    Rectangular blocks (8x8 pixels)
    Every n scanlines
The R is responsible for rendering inside tile
A triangle can be sent to many FG’s depending on overlap (over tiles)

## Slide 13: Sort-Last Fragment
Sorts betwen FG and FM
XBOX uses this!
Again spread work among G’s
The generated work is sent to FG’s
Then sort fragments to FM’s
  An FM is responsible for a tile of pixels
A triangle is only sent to one FG, so this avoids doing the same work twice
  Sort-Middle: If a triangle overlaps several tiles, then the triangle is sent to all FG’s responsible for these tiles
  Results in extra work

## Slide 14: Sort-Last Image
Sorts after entire pipeline
So each FG & FM has a separate frame buffer for entire screen (Z and color)
After all primitives have been sent to pipeline, the z-buffers and color buffers are merged into one color buffer
Can be seen as a set of independent pipelines
Huge memory requirements!
Used in research, but probably not commerically

## Slide 15: Memory bandwidth usage is huge!!
R is read, W is write, T is texture, Z is Z-buffer, C is color buffer
Assuming 2 textures per pixel, and TR costs 24 bytes (triline MIP-mapping), the rest costs 32 bits (4 bytes)
A ”normal” pixel costs:
  ZR+ZW+CW+2*TR=60 bytes per pixel
At 60 fps, 1280x1024: 4.5 Gb/s
But a pixel is overwritten many times!
Overdraw=4 gives: 18 Gb/s !
Then assume DDRAM at 300 MHz, 256 bits per access: 9.6 Gb/s
18>9.6 !!

## Slide 16: Memory bandwidth, cont’d
18>9.6
On top of that bandwith usage is never 100%, and we can also use more textures, anti-aliasing, to use up even more bandwidth
However, there are many techniques to reduce bandwith usage:
  Texture caching with prefetching
  Texture compression
  Z-compression
  Z-occlusion testing (HyperZ)

## Slide 17: Z-occlusion testing and Z-compression
One way of reducing bandwidth
  ATI Inc., pioneered with their HyperZ technology
Very simple, and very effective
Divide screen into tiles of 8x8 pixels
Keep a status memory on-chip
  Very fast access
  Stores additional information that this algorithm uses
Enables occlusion culling on triangle basis, z-compression, and fast Z-clears

## Slide 18: Architecture of Z-cull and Z-compress
Store zmax per tile, and a flag (whether cleared, compressed/uncompressed)
Rasterize one tile at a time
Test if zmin on triangle is farther away than tile’s zmax
  If so, don’t do any work for that tile!!!
  Saves texturing and z-read for entire tile – huge savings!
Otherwize read compressed Z-buffer, & unpack
Write to unpacked Z-buffer, and when finished compress and send back to memory, and also: update zmax
For fast Z-clears: just set a flag to ”clear” for each tile
  Then we don’t need to read from Z-buffer, just send cleared Z for that tile

## Slide 19: The Xbox game console
Built by Microsoft and NVIDIA
Is almost a PC:
  Pentium III, 733 MHz
  An extended GeForce3
Why a console then?
  It stays constant…
  You don’t have to care about 20 different graphics cards, and CPUs from 100 MHz to 2GHz

## Slide 20: Xbox is a UMA machine
UMA = unified memory architecture
  Every component in the system accesses the same memory
We focus on the
GPU

## Slide 21: Xbox Graphics Processing Unit (GPU)
Supports programmable vertex shaders
  No fixed-function geometry stage
Is sort-last fragment architecture
Rasterizer: handles four pixels per clock
Runs at 250 MHz

## Slide 22: Xbox geometry stage
Dual vertex shaders
  Same vertex program is executed on two vertices in parallell
Vertex shader unit is a SIMD machine that operates on 4 components at a time
  The point is that instead of a fixed function geometry stage, we have now full control over animation of vertices and lighting etc.
Uses DMA (direct memory access), so that the GPU fetches vertices directly from memory by itself!
Three different caches – for better performance!

## Slide 23: Xbox geometry stage: caches
Pre T&L (transform & lighting)
  Stores vertices fetched from mem
  The idea is the avoid redundant memory fetches
  A vertex is, on average, shared by 6 triangles
  Has 4 kbytes of storage
Post T&L cache:
  Avoid running vertex shader more than once for same vertex
  So it has storage for 16 transformed vertices
Primitive Assembly cache:
  A transformed vertex requires a lot of memory, and so it takes a while to fetch a vertex from the Post T&L cache
  Can store 3 fully shaded vertices
  Is there to avoid fetches from Post T&L
Task of PA cache is to feed rasterizer with triangles

## Slide 24: Xbox rasterizer
First block: triangle setup (TS) and FG
TS computes various deltas (see slide 6) and other startup info
This block also does Z-occlusion testing
FG generates fragments inside triangles
  Tests 2x2 pixels at a time, and forwards these to the four pipelines that follow
  Note: near edges, not all pixels are inside triangles, and therefore 0-3 pipelines may be idle
  There are many strategies on how to find which fragments are inside triangle, but exactly how this is done on the XBOX is not known

## Slide 25: Xbox rasterizer
Sorting is done after FG
  Sort-last fragment arch.
First: 2 texture units
  Can be run twice  4 texture lookups
RC (register combiners) operate on the filtered texel values from TC and from interpolated shading over triangle (programmable too)
  Can be used for bump mapping, for example
Finally, result from TXs, RCs, shading interpolation, fog interpolation is merged into a final color for that pixel

## Slide 26: Xbox rasterizer: Fragment merge
The combiner produced a final color for the pixel on a triangle
FG merges this with:
  Color in color buffer (alpha blending)
  Respect to Z-buffer
  Stencil testing
  Alpha testing
Z-compression and decompression is handled here as well
Writes final color over the system memory bus

## Slide 27: Xbox texture swizzling
A technique to improve usage of locality in textures
  Not likely that we will access texels in a linear fashion (i.e., one scanline at a time)
  Use swizzling instead
Assume (u,v)=(un-1…u1u0, vn-1…v1v0)
  ui and vi are bits i of u and v
Linear (normal): (width*v+u)*bytes_per_color
Instead: (un-1vn-1…u1v1u0v0)* bytes_per_color

## Slide 28: Xbox texture swizzling
This access technique gives the following pattern (4 bytes/color)
This is a space-filling curve, and those are often designed so that coherency usage is improved
Example: bilinear filtering
Almost a Hilbert curve

## Slide 29: Xbox conclusion
(Almost) a PC with great graphics hardware
Sort-last fragment architecture
2 vertex shaders
4 pixel pipelines @ 250 MHz
Programmable per pixel as well
One of the best consoles right now…
  Not for long though

## Slide 30: KYRO – a different architecture
Based on cost-effective PowerVR architecture
Tile-based
  For KYRO II: 32x16 pixels
Fundamental difference
  For entire scene, do this:
  Find all triangles inside each tile
  Render all triangle inside tile
Advantage: can implement temporary color, stencil, and Z-buffer in fast on-chip memory
Saves memory and memory bandwidth!
  Claims to save 2/3 of bandwidth compared to traditional architecture (without Z-occlusion testing)

## Slide 31: KYRO architecture overview
CPU sends triangle data to KYRO II
Tile Accelerator (TA)
  Need an entire scene before ISP and TSP blocks can start
  So TA works on the next image, while ISP and TSP works on the current image (i.e., they work in a pipelined fashion)
  TA sorts triangles, and creates a list of triangle pointers for each tile (for tris inside tile)

## Slide 32: KYRO
Tile accelerator:
  When all triangle for entire scene are sorted into tiles, the TA can send tile data to next block ISP
  And the TA then continues on the next frame’s sorting in parallel
Image synthesis processor (ISP):
  Implements Z-buffer, color buffer, stencil buffer for tile
  And occlusion culling (similar to Z-occlusion testing)
    Test 32 pixels at a time against Z-buffer
    Records which pixels are visible
  Groups pixels with same texture and sends to TSP
    These are guaranteed to be visible, so we only texture each pixel once

## Slide 33: KYRO: TSP
Texture and Shading Processor (TSP):
  Handles texturing and shading interpolation
Has two pipelines that run in parallell
  2 pixels per clock
Can use 8 textures at most
  Is implemented by ”looping” in TSP
  I.e., not full speed
Texture data is fetched from local memory
Supersampling: 2x1, 1x2, and 2x2
  Renders a larger image and filters and scales down
  For 2x2: Need only 4x the size of tile (or rather, render 4x as many tiles, i.e., need not 4x memory)

## Slide 34: KYRO: pros and cons
Uses a small amount of very fast memory
  Reduces bandwidth greatly
  Reduces frame buffer memory greatly
But more local memory is needed
  For tile sorting
  Amount of local memory places a limit on how many triangles can be rendered
  3 MB can handle a little over 30,000 triangles
Design is parallel
  Add more pipelines that can handle the rest of the architecture that follows the Tile Accelerator
  But bottleneck will (likely) move, and so not sure how much can be gained

## Slide 35: Challenges for the future
Continue to push the frontier of ”normal” graphics hardware
  How long can the ”2x performance per 6 months” keep up?
  Keep adding new features…
  Next generation is expected to be massively programmable, both at vertices and at pixels
  Another goal is to make rendering more realistic
    Do this by developing new algorithms for the programmable hardware

## Slide 36: Challenges for the future
Design a new architecture targeted for global illumination
Very few have focused on ”ray tracing”- based algorithms so far
It is time now…
Would be nice with:
  Rapid intersection testing of curved surfaces in hardware
  Rapid traversal of spatial data structure
  Handling of very large scenes
    Standard graphics hardware can handle quite good because a triangle can be discared once it has been rendered
    Ray tracing-based algorithms cannot do this, because it renders shadows and reflections and therefore need to know of geometry nearby
  Photon mapping…

## Slide 37: Challenges for the future
Design really small architectures with really scarce resources
  Little chip area
  Little memory
  Little bandwidth
So that it can be used in mobile devices, e.g., PalmPilot’s, phones, etc.

## Slide 38: Graphics hardware conclusion
Possible to build great hardware for standard triangle rendering
  Reasons: pixel independency, parallellism, pipelining, etc.
Ray tracing-based hardware will come
  It has been shown that commodity graphics hardware can be used for ray tracing
  See paper by Tim Purcell et al., SIGGRAPH 2002
Not sure what will happen in the future, but it will happen pretty fast
  ”it will be utterly fantastic”