## Slide 1: Biorefinery, the bridge between agriculture and chemistry
Marieke Bruins, 18-9-2013

## Slide 2: Biomass use today and in 2050
  Mton
Food incl. feed* 5000
Wood, paper, cotton 2000
Wood for cooking 4000
30% of 1000EJ in 2050= 20 000
All bulk chemicals in 2050 600(= 2000 input!)
* Excluding grass and seafood
Only increasing field yields will not satisfy demands

## Slide 3: How to make better use of biomass under sustainable conditions?
Biorefinery as a tool
  Four rules for good biorefinery
  Examples
Small scale as a special case

## Slide 4: Biorefinery
Biorefining: Sustainable processing of biomass into a spectrum of bio-based products (food, feed, chemicals, materials) and bioenergy (biofuels, power and/or heat).

## Slide 5: How to compete with fossil under sustainable conditions?
  Choose the right raw material
  Use all biomass components
  Use each component at its highest value:
  (molecular) structure is much better than caloric value
  However, keep components on the field that are required for soil fertility

## Slide 6: How to compete with fossil under sustainable conditions?
  Choose the right raw material
  Use all biomass components
  Use each component at its highest value:
  (molecular) structure is much better than caloric value
  However, keep components on the field that are required for soil fertility

## Slide 7: Raw material
Sugarcane, corn for sugar, starch based biorefinery: Often better used as food
The alternative: Lignocellulosic feedstock: development of pre-treatment methods needed

## Slide 8: Lignocellulose hydrolysate, not an ideal substrate yet
Mixing problems, low oxygen transfer, low substrate concentrations, fermentation inhibitors
Complex: implications for product recovery

## Slide 9: Why do aerobic fermentations have low Ys
Lysine: 0.45 g/g
Glutamic acid: 0.48 g/g
While anaerobic fermentations have high yields
Lactate: 0.95 g/g
Ethanol: 0.95 J/J

## Slide 10: Anaerobic fermentations
 |  | Aerobic |  | Anaerobic
Productivity | ✗ | Limited by O2 transfer | ✔ | No O2 required
 | ✗ | Limited by cooling capacity | ✔ | Low heat production
Substrate efficiency | ✗ | High biomass production | ✔ | Low biomass production
 | ✗ | Complete oxidation of substrate to CO2 | ✔ | No complete oxidation

## Slide 11: Anaerobic fermentations
Productivity: up to 5 times higher as compared to aerobic
Less cooling equipment
No compressor
Much less stirring
Leading to much lower capital costs per ton of product

## Slide 12: Green Biorefinery
Teekens et al. (in preparation)

## Slide 13: How to compete with fossil under sustainable conditions?
  Choose the right raw material
  Use all biomass components
  Use each component at its highest value:
  (molecular) structure is much better than caloric value
  However, keep components on the field that are required for soil fertility

## Slide 14: Grass: few products or many ?

## Slide 15: Grass Biorefinery
EVAPORATION
PROTEIN RECOVERY
CUTTING
TRANSPORT
REFINING
JUICE FRACTION
FIBER FRACTION
CULTURE
SEPARATION
patent pending
PRESERVATION
STORAGE
FRACTIONATION
DRYING
DOWN STREAM
PROCESSING
2°-generation products
green grass protein
compound feed
white grass protein
Grass protein (products)
Fibre (products)
Grass juice concentrate

## Slide 16: Grass Biorefinery
Mobile pilot GRASSA! Oenkerk (2011)

## Slide 17: Grass: few products or many ?

## Slide 18: Biorefinery enables power generation at 45€/ton and high quality 2nd generation fermentation raw materials for 200€/ ton
Chart: €/GJ
| 0.7 | 1.8 | 2.6
Y-waarde 1 | 2.7 | 3.2 | 0.8
Y-waarde 2 | 1 | 1 | 1
Multiproduct
biorefinery
Wood
chips
Straw
(field)
Straw
(collected)
Straw
(washed)
Rape
meal
Animal
feed
Protein
Amino
acids
Ferment.
substrates
Ligno-
cellulose
Fibres
Phosphorus
Rest
3

## Slide 19: How to compete with fossil under sustainable conditions?
  Choose the right raw material
  Use all biomass components
  Use each component at its highest value:
  (molecular) structure is much better than caloric value
  However, keep components on the field that are required for soil fertility

## Slide 20: Protein recovery from biomass
Biorefinery is not just producing biofuels
For economic feasibility
protein recovery and use
is an essential part of
the overall biorefinery
Research
  Several biomass sources, preferably “waste”
  Protein hydrolysis to amino acids
  Selective recovery through e.g. crystallization or electrodialysis
  Always in a bigger picture: with the other components

## Slide 21: Protein from Tea residue
One-step extraction for LP
Multiple-extraction for multiple products:
Extract
Powder
(freezing dry)
Pigment
Polyphenol
Pectin
Protein
Raw material
Final residue
Also other components
General mechanisms for leaves

## Slide 22: Integrated conversion and separation
CEM
-
-
-
-
-
AEM
+
+
+
+
+
CEM
-
-
-
-
-
AEM
+
+
+
+
+
+
Anode
-
Cathode

## Slide 23: Use of plant molecular structures
Diaminobutane
Acrylonitrile
N-Methylpyrrolidone
N-Vinylpyrrolidone
Glutamic acid

## Slide 24: The route to NMP, new vs conventional
New route
Conventional route
Glutamic acid
NMP
Amino acids contain N and O.  Less steps (= factories) & energy for the same product!
step 1
step 2

## Slide 25: Biobased NMP, makes an ethanol plant profitable
36 kton glutamic acid 
23 kton NMP
(~2500 € / ton)
=58 M€/y
500 Million liters bioethanol
(~ 400 kton) =200M€
360 kton DDGS (~130 € / ton) =46M€

## Slide 26: How to compete with fossil under sustainable conditions?
  Choose the right raw material
  Use all biomass components
  Use each component at its highest value:
  (molecular) structure is much better than caloric value
  However, keep components on the field that are required for soil fertility
Do not transport what you do not need

## Slide 27: Small scale biorefinery
Starch from Cassava in Nigeria
Solving the problem of low functional density of biomass
Advantages
  Lower transportation costs
  Water and minerals stay on site
  Less waste treatment on (central) factory
  Increased storage times
  More income to farmers
  Faster innovations
Disadvantage
  Economy of scale
Notes: BioRegional MiniMills UK Ltd broke new ground this month, securing an investment deal that puts the company in a good position to finally commercialise the MiniMill technology, which pulps materials other than wood into paper and recovers energy from the black liquor waste. In the UK up to 20% of imported wood pulp could be replaced by straw, creating a market worth £27m to UK farmers.
Grassa en zeafuels

## Slide 28: Advantage: lower transportation cost
Separate before transportation (biomass pre-treatment)

## Slide 29: Small scale biorefinery reduces transport cost and seasonality
Concept
Small scale processing
100%
Return flow 70%
30%
Fields
Processing
Present
100%
100%
Return flow 10%
Farm
concentration
fermentation

## Slide 30: Advantage: lower transportation cost
Separate before transportation (biomass pre-treatment)
Local biomass and local product
Fuels
  Biogas
  Ethanol
  PPO
  Pellets/pyrolysis

## Slide 31
Central Kalimantan
Mega Rice Project (1996-1998)
rubber
oil palm
Jatropha

## Slide 32
Available
Small farmers
Waste

## Slide 33: Breakthroughs in biofuels: Mobile technology for biodiesel production from Indonesian resources
(local)
markets

## Slide 34: Agriculture beyond food
Two worlds meet:
Mobile biodiesel refining
Protein extraction
Oil Crops
Rubber
Jatropha
Oil palm
Mobile
Seed Processing unit
Biodiesel synthesis and work-up
Protein
Protein work-up
(local) markets

## Slide 35: Advantage: water and minerals stay on site

## Slide 36: Advantage: water and minerals stay on site
Drying: Transport advantage
Dewatering: Additional advantages
Do not take from the field what you do not need
Another advantage:
less waste treatment

## Slide 37: Advantage: increased storage times
WO2005/121183A1

## Slide 38: Advantage: increased storage times
Sugar beet processing in the Netherlands
  September-December/January max. 5 months
Kolfschoten et al (in preparation)

## Slide 39: Advantage: more income to farmers
Redistribution of income in the chain
More jobs in rural areas
Less dependent on industrial contracts down stream
Incentive to increase productivity
Farmers are entrepreneurs:
  Biogas
  TKI small scale biorefinery
  Important stakeholders

## Slide 40: Advantage: faster innovation
“Factory at the size of a pilot plant”
Low absolute CAPEX
Easier to change
Can be improved with subsequent factories

## Slide 41: Disadvantage: economy of scale

## Slide 42: Design rules for scaling in biorefinery
Advantages of small scale without the disadvantages
Splitting the process in two parts
Low investment cost
Minimize heat exchange
Energy use and the combination with biogas and CHP
Developments start bottom-up
Bruins & Sanders (2012) BioFPR 6(2):135-145
Notes: There is no water in the petrochemical industry

## Slide 43: Biorefinery, the bridge between agriculture and chemistry
  Choose the right raw material
  Use all biomass components
  Use each component at its highest value:
  (molecular) structure is much better than caloric value
  However, keep components on the field that are required for soil fertility

## Slide 44: Biorefinery, the bridge between agriculture and chemistry, Biorefining, from raw material to high value products
  Choose the right raw material
  Use all biomass components
  Use each component at its highest value:
  (molecular) structure is much better than caloric value
  However, keep components on the field that are required for soil fertility