## Slide 1: Jerusalem artichoke as raw material in the biorefinery concept
Ingólfur Bragi Gunnarsson
Ph.D. student
Supervisor: Prof. Irini Angelidaki
Co-supervisor: Dimitar Karakashev

## Slide 2: The Biorefinery concept:
Is similar to today’s petroleum refineries
Instead of using petroleum, the numerous refinery products are produced from BIOMASS
A biorefinery should produce a number of products
  e.g. biofuels, biochemicals, feed or other products
Production of high-added-value product/s
  Otherwise the process becomes uneconomical

## Slide 3: Biomass Jerusalem artichoke
                High biomass production yields
                Low maintenance crop
                Frost and drought tolerant

## Slide 4: But....
When to harvest?
Where are the valuable compounds?

## Slide 5: Our biomass
11 different clones
3 harvesting occasions
Lignocellulosic- and tuber fractions

## Slide 6: Lignocellulosic biomass
Chart: g/g dw
| Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Johan A | Bianca | Dragon | Rema | Topstar | Urodny | Vanlig | Kung Ale | Kåseberga | Lars Törner | Larsviken
Cellulose | 0.14471 | 0.21946 | 0.28463 | 0.18219 | 0.17195 | 0.26693 | 0.22729 | 0.18921 | 0.29437 | 0.16227 | 0.12133 | 0.1651 | 0.14202 | 0.19809 | 0.2958 | 0.15776 | 0.13544 | 0.22413 | 0.17458 | 0.19142 | 0.21056 | 0.14695 | 0.16183 | 0.23575 | 0.11615 | 0.15789 | 0.1791 | 0.12414 | 0.19621 | 0.27476 | 0.15347 | 0.20209 | 0.29513
Hemicellulose | 0.16832 | 0.14351 | 0.11503 | 0.1238 | 0.13414 | 0.14593 | 0.1228 | 0.16316 | 0.093028 | 0.11615 | 0.11775 | 0.095271 | 0.13191 | 0.11574 | 0.093344 | 0.11669 | 0.10256 | 0.10515 | 0.13122 | 0.11634 | 0.12102 | 0.11132 | 0.10007 | 0.14102 | 0.1017 | 0.10843 | 0.11471 | 0.1061 | 0.13752 | 0.11315 | 0.13186 | 0.15442 | 0.094774
Lignin | 0.18369 | 0.18121 | 0.17473 | 0.15562 | 0.14539 | 0.17621 | 0.12213 | 0.12399 | 0.16304 | 0.15862 | 0.17963 | 0.19232 | 0.17716 | 0.18194 | 0.18668 | 0.1326 | 0.17583 | 0.20731 | 0.16045 | 0.17061 | 0.19288 | 0.13597 | 0.15017 | 0.19169 | 0.22057 | 0.2151 | 0.19758 | 0.18963 | 0.20224 | 0.20516 | 0.18578 | 0.1977 | 0.2028
Protein | 0.032 | 0.015938 | 0.013656 | 0.0475 | 0.022187 | 0.012406 | 0.058 | 0.035625 | 0.029281 | 0.03875 | 0.0325 | 0.020156 | 0.02125 | 0.028125 | 0.011562 | 0.023438 | 0.022187 | 0.019719 | 0.04 | 0.032813 | 0.012344 | 0.0315 | 0.024063 | 0.016625 | 0.0225 | 0.019688 | 0.014344 | 0.06125 | 0.027187 | 0.012844 | 0.0275 | 0.025 | 0.011187
Lipids | 0.044458 | 0.043843 | 0.03475 | 0.035783 | 0.028685 | 0.022179 | 0.044502 | 0.038574 | 0.03676 | 0.045201 | 0.044927 | 0.035667 | 0.03652 | 0.028519 | 0.022415 | 0.045713 | 0.038533 | 0.038272 | 0.043845 | 0.042488 | 0.034336 | 0.034075 | 0.027483 | 0.021105 | 0.042423 | 0.036551 | 0.036461 | 0.038308 | 0.040907 | 0.035765 | 0.044714 | 0.042105 | 0.034703
Uronic acids | 0.10443 | 0.1288 | 0.11985 | 0.14893 | 0.14168 | 0.090931 | 0.14922 | 0.11042 | 0.13903 | 0.15572 | 0.15583 | 0.14107 | 0.14099 | 0.15311 | 0.14134 | 0.15725 | 0.16537 | 0.13171 | 0.14637 | 0.15601 | 0.11848 | 0.15671 | 0.17264 | 0.091585 | 0.16591 | 0.15909 | 0.12282 | 0.15993 | 0.13851 | 0.12528 | 0.14347 | 0.1148 | 0.13588
Extractives | 0.12547 | 0.12744 | 0.11423 | 0.11455 | 0.11143 | 0.10282 | 0.11751 | 0.11052 | 0.10031 | 0.13131 | 0.13444 | 0.12069 | 0.12035 | 0.11405 | 0.10697 | 0.12426 | 0.11365 | 0.10751 | 0.12737 | 0.12714 | 0.11619 | 0.11229 | 0.1099 | 0.10072 | 0.11532 | 0.10781 | 0.10242 | 0.1245 | 0.13029 | 0.1138 | 0.13106 | 0.13138 | 0.11218
Ash | 0.10612 | 0.084346 | 0.051645 | 0.11513 | 0.081458 | 0.06859 | 0.11638 | 0.083704 | 0.046938 | 0.13676 | 0.096732 | 0.062797 | 0.10901 | 0.12654 | 0.050808 | 0.13042 | 0.14795 | 0.028532 | 0.13467 | 0.10561 | 0.054336 | 0.12849 | 0.094518 | 0.079329 | 0.10045 | 0.11214 | 0.073446 | 0.13151 | 0.1031 | 0.055293 | 0.13515 | 0.088357 | 0.066495
Other | 0.090814 | 0.05544 | 0.091489 | 0.076494 | 0.16308 | 0.114 | 0.042167 | 0.14479 | 0.097241 | 0.055215 | 0.11687 | 0.16693 | 0.12079 | 0.053888 | 0.091079 | 0.11187 | 0.098482 | 0.13767 | 0.041483 | 0.057573 | 0.13985 | 0.14269 | 0.15931 | 0.12218 | 0.11499 | 0.0833 | 0.15911 | 0.064642 | 0.024035 | 0.063949 | 0.046988 | 0.044151 | 0.046845

## Slide 7: Tuber biomass
Chart: g/g dw
| Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Sept. | Oct. | Dec. | Johan A | Bianca | Dragon | Rema | Topstar | Urodny | Vanlig | Kung Ale | Kåseberga | Lars Törner | Larsviken
Inulin | 0.82417 | 0.81142 | 0.80213 | 0.81144 | 0.80515 | 0.80729 | 0.80703 | 0.79492 | 0.80317 | 0.81096 | 0.76347 | 0.79876 | 0.83775 | 0.81603 | 0.83231 | 0.84475 | 0.78802 | 0.81884 | 0.80271 | 0.77331 | 0.79638 | 0.81721 | 0.80002 | 0.78688 | 0.84051 | 0.81704 | 0.83526 | 0.85481 | 0.83139 | 0.81171 | 0.84641 | 0.78584 | 0.78801
Protein | 0.061875 | 0.085625 | 0.071208 | 0.0675 | 0.0675 | 0.068792 | 0.083125 | 0.059062 | 0.05775 | 0.085 | 0.086875 | 0.080969 | 0.084375 | 0.0675 | 0.060083 | 0.07875 | 0.052812 | 0.089917 | 0.088438 | 0.059062 | 0.10325 | 0.09375 | 0.070312 | 0.1001 | 0.074375 | 0.06625 | 0.079917 | 0.070825 | 0.080625 | 0.087625 | 0.07144 | 0.07755 | 0.080094
Free sugars | 0.039492 | 0.048982 | 0.050481 | 0.03972 | 0.049183 | 0.049576 | 0.040177 | 0.050964 | 0.049058 | 0.049009 | 0.037075 | 0.04547 | 0.043516 | 0.041281 | 0.045323 | 0.052764 | 0.042326 | 0.051321 | 0.047609 | 0.034612 | 0.048142 | 0.048119 | 0.040693 | 0.048399 | 0.053909 | 0.04584 | 0.052847 | 0.041756 | 0.050855 | 0.048102 | 0.041731 | 0.04732 | 0.045686

## Slide 8: Biomass yields
Most lignocellulosic biomass in first harvest
  Highest amount DW biomass in last harvest!
  Not enough to only look at mass (water content matters).
Most tuber biomass in last harvest
  Inulin had highest degree of polymerization at first harvest
High cellulose production yields (Mg/ha)

## Slide 9: Products so far…
Inulin (high or low degree of polymerization)
  Depends on harvesting occasion
  Different applications
Protein as high as 10% of DW in tubers
What else?

## Slide 10: Conversion
Bioethanol (CH3CH2OH + CO2)
Biogas (CH4 + CO2)
  Produced from waste streams
  Autogas (Pure methane)
  Biogas upgrading (expensive)
Biosuccinic acid
  What is that?
  Why?
  How?
Notes: Figure for biogas upgrading!
Biogas: wide spread application, waste used to produce biogas.
Biogas contains methane and co2. however for use in other applicaiton (autogas) we need to remove co2.
Other processes exist but they are expensive and only capture it (not environmentally friendly). Many cases co2 and some ch4 ends up being released into athmosphere.

## Slide 11: Succinic acid
Currently produced from petrochemicals!
Applications for SA include:
  Pharmaceuticals, coatings, biopolymers,resins and solvents.

## Slide 12: Biosuccinic acid production
Succinic acid producing bacteria
  Actinobacillus succinogenes
  Anaerobiospirillum succinoproducens
  Mannheimia succiniciproducens
  recombinant Escherichia coli strains
  recombinant Corynebacterium glutamicum
A. Succinogenes 130Z
  Ordered from DSMZ
  Fixates CO2 during fermentation
  Can utilize a variety of substrates under anaerobic conditions
  High tolerance to substrate
  High succinic acid tolerance

## Slide 15: Patented technology
Fermenter
Feedstock
Biogas (CH4/CO2)
CH4
Effluent containing Succinic acid
SA bacterium

## Slide 16: Simultaneous biogas upgrading and succinic acid production
Chart: 6.7L Biogas upgrading (GC)
| 0.0 | 10.0 | 11.0 | 13.5 | 15.0 | 16.0 | 16.5 | 17.0 | 17.5 | 18.0 | 18.5 | 19.0 | 20.0 | 24.0 | 36.0
%CH4 | 0.69827 | 0.74705 | 0.74826 | 0.74966 | 0.61861 | 0.61983 | 0.62588 | 0.6408 | 0.65683 | 0.66802 | 0.68982 | 0.70904 | 0.76402 | 0.94632 | 0.99643
%CO2 | 0.30173 | 0.25295 | 0.25174 | 0.25034 | 0.38139 | 0.38017 | 0.37412 | 0.3592 | 0.34317 | 0.33198 | 0.31018 | 0.29096 | 0.23598 | 0.053676 | 0.0035662
OD660nm | 0.159 | 0.129 | 0.425 | 0.548 | 0.6 | 0.699 | 0.735 | 1.1 | 1.25 | 1.61 | 1.755 | 1.92 | 2.178 | 2.52 | 2.75 | 2.94 | 3.29 | 3.7 | 4.2 | 4.4 | 4.96 | 5 | 5.86 | 5.54 | 3.62
Chart: Succinic acid fermentation during biogas upgrading (HPLC)
| 0.0 | 10.0 | 12.25 | 13.25 | 14.0 | 15.0 | 16.0 | 16.5 | 16.75 | 17.5 | 18.0 | 18.25 | 18.5 | 18.75 | 19.0 | 20.0 | 24.0 | 36.0
Glucose | 29.7678 | 31.256 | 30.3738 | 28.9809 | 27.9653 | 27.9607 | 28.627 | 28.0985 | 24.6479 | 26.7911 | 23.8592 | 24.1679 | 23.3455 | 22.0091 | 22.9399 | 19.276 | 11.5476 | 5.71 | 25.4409
Succinate | 0.28173 | 0.21359 | 0.21563 | 0.26118 | 0.36691 | 0.66678 | 1.0189 | 1.3112 | 1.476 | 2.1492 | 2.465 | 2.8441 | 3.0993 | 3.2408 | 3.6832 | 4.8735 | 7.9261 | 8.9565
Formate | 0.072173 | 0.093942 | 0.058645 | 0.10733 | 0.047864 | 0.22895 | 0.45673 | 0.55088 | 0.68774 | 1.1145 | 1.3863 | 1.602 | 1.7951 | 1.8695 | 2.0476 | 3.1764 | 5.5816 | 7.5995
Acetate | 0.106 | 0.10512 | 0.12196 | 0.21222 | 0.18345 | 0.31786 | 0.53096 | 0.70577 | 0.8054 | 1.2203 | 1.4968 | 1.7269 | 1.8678 | 1.9581 | 2.2232 | 3.0978 | 5.4032 | 6.6701
Ethanol | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0671 | 0.1668 | 0.1908 | 0.2249 | 0.2207 | 0.2501 | 0.287 | 0.5164 | 1.2396 | 2.4296
OD660nm | 0.159 | 0.129 | 0.425 | 0.548 | 0.6 | 0.699 | 0.735 | 1.1 | 1.25 | 1.61 | 1.755 | 1.92 | 2.178 | 2.52 | 2.75 | 2.94 | 3.29 | 3.7 | 4.2 | 4.4 | 4.96 | 5 | 5.86 | 5.54 | 3.62

## Slide 17
Fermentation of tuber hydrolysates:
SA yield was 80.2% in bottles compared to 77.9% in 3-L bioreactor.
However the SA production was increased by 26.4% in 3-L bioreactor and the D-fructose utilization increased from 68.5% to 96.5%.
Chart: 3-L bioreactor
| Initial reducing sugar | Residual reducing sugar | Succinic acid | Formate | Acetate | 0 hours | 48 hours
 | 4.528 | 0.2 | 26.8 | 5.6 | 8.5
 | 31.1808 | 1.1
Chart: Batch bottles
| Initial reducing sugar | Residual reducing sugar | Succinic acid | Formate | Acetate | 0 hours | 48 hours
 | 5.6324 | 0.3 | 21.1602 | 3.587 | 6.7956
 | 30.7475 | 9.6994

## Slide 18: Summary
Composition analysis
Harvest occasion very important
Difference between clones not significant
Reduction in CO2 emissions
Simultaneous biogas upgrading and succinic acid production
The potential is definitely there!

## Slide 19: Thank you!